## Slide 1
NOWHERE
TO GO
The Tura rises at 370 m in the Ural mountains and flows east past Tyumen, my home city, into the Tobol. The Tobol flows into the Irtysh, and the Irtysh into the Ob, which carries all of it north to the Kara Sea in the Arctic — four rivers, one journey from source to sea. It does four-fifths of its falling in the first 98 km. After that it drops 5cm/km — so, when the water rises it cannot flow away downstream. It spreads. That is why half of Russia’s marshland is here, and why Tyumen went under in August 2026.
SASHA OSTRIAGIN
Bromsgrove School
TYUMEN · city
Oldest Russian city in Siberia, 1586.
TURA · river
Tyumen’s river. 1,030 km, from the Urals.
TOBOL · river
The river the Tura runs into. 1,591 km.
IRTYSH · river
4,248 km, from China. Takes the Tobol.
OB · river
3,650 km more, to the Arctic Ocean.
WHAT THE GRADIENT BUILDS
Steep upper course: vertical erosion cuts a V-shaped valley. Once the gradient collapses, lateral erosion takes over — the river meanders and widens a floodplain, then abandons it. Those are the river terraces Tyumen is built on.
WHY SO MUCH OF IT DROWNS
With almost no slope the channels cannot clear meltwater or rain: half of all the marshland in Russia is in this basin. The Ob also flows north, so meltwater from the thawing south meets 2 m of ice and spreads up to 50 km sideways.
WHO WANTS THE WATER
27 million people; two-thirds of Russia’s oil and gas. Flat ground allows just one dam on 3,650 km of Ob. Upstream, China’s Irtysh–Karamay canal takes 2.5 km³ a year from the longest transboundary tributary on Earth, with no treaty.
WHAT HAPPENED AT TYUMEN
Rain on the headwaters in the Ural mountains. 700km downstream the Tura rose for three weeks and peaked at 897 cm on 2 August 2026 — a record summer flood.
18 JUNE
137 ha
29 JULY
415 ha — tripled
1 in 6
buildings flooded on the low bank, against 1 in 250 on the high bank. Nine times as many people were in the water.
Tyumen’s low bank sits 11 m above the river.
So does Frankwell, in Shrewsbury.
WHAT COULD HAPPEN HERE
The Severn at Shrewsbury has the same shape as the Tura at Tyumen: a medieval town on the high bank, and a district on the low bank that floods. Same section, different country.
6.3m → 8m
English properties in areas at risk of flooding today, and by mid-century on the Environment Agency’s own projection — one property in four.
What the two sections say. Height above the river predicts flooding better than any map, and it costs nothing to measure — the elevation data is global and open. The question is not whether a river floods, but how far above it we are building, and where the next river terrace up begins.
Method. Copernicus DEM GLO-30 elevations; flood extent from Sentinel-2 L2A using MNDWI (Xu 2006). Imagery and elevation data © European Union / ESA, free and open licence; every map and section here is my work from them.
Sources: Britannica; WWF/TNC Freshwater Ecoregions of the World; Eurasian Development Bank 2025; Environment Agency NaFRA 2024.